## Slide 1: Trading Utilization for Circuitry: Hardware-Software Co-design for Real-Time Software-Based Short-Circuit Protection
Aaron Willcock
Department of Computer Science, Wayne State University, USA

## Slide 2: Toast, anyone?
?
?
Notes: Have you ever been tempted to toss a toaster into the tub?
Perhaps silverware in a socket is more your style?
You don’t have to admit it here. But if you found yourself considering it, know that there are safety mechanisms to stop the short circuits you’d create making it much less exciting.

## Slide 3: Not Your Fault
Ground Fault Interrupter
Fuse Box
Image Provided by: Dimitry G https://commons.wikimedia.org/wiki/File:Fuse_box_after_finishing.JPG
Goal: Stop short circuits, avoid damage (death) via fixed hardware
Notes: If your house or apartment was constructed more recently, it likely has Ground Fault Interrupters and Fuse Boxes aimed at stopping short circuits before they cause damage. These protection mechanisms, however, is fixed hardware. This is not the Internet of Things nor a SMART home feature.

## Slide 4: Your Home is Not Alone
Home Applications:
  Photovoltaics
Industrial Electronics:
  Devices using Insulated Gate Bipolar Transistors (IGBTs)
In General:
  Power Converters / Inverters (AC → DC, DC → AC)
Notes: But your home is not alone in this short-protection technology. Outside the house, photovoltaic systems require short protection as do industrial electronics like IGBTs. In general, systems that conduct power conversion have some short-circuit hardware in place to prevent damage and death.

## Slide 5: Low Power, High Stakes
Embedded systems need protection
Ex. Samsung Galaxy Note 7
  Batteries caught fire
  Device banned by FAA
  Root cause: short circuits
Image Provided by: Independent.co.uk https://www.independent.co.uk/life-style/gadgets-and-tech/news/samsung-galaxy-note-7-return-refund-exploding-fire-brand-recall-a7361216.html
Notes: Short circuits are not just a problem for houses. Embedded systems need protection as well! As an example, the Samsung galaxy note 7 made headlines when its batteries caught fire or exploded. The device was even banned by the FAA. After internal investigations, Samsung declared short circuits in the battery as the cause. Despite the lower power, short circuits can still cause substantial damage

## Slide 6: Motivation and Problem Statement
Image Provided by: WEETECH Inc.
https://www.weetech-usa.com/applications/ automotive/relay-and-fuse-box/
Short
  Damage
  Time-sensitive
Dedicated circuitry
  Inflexible
  Costly
  Pessimistic
Existing short-circuit protection for embedded systems is fixed, inflexible and does not consider software-based real-time control.
Problem Statement:
Notes: It’s well established that short circuits can cause damage and even death. What’s worse is that hardware-based approaches are inflexible, costly, and pessimistic. Consider automotive fuses for example. These fuses consume a great deal of space in a vehicle (and similarly in embedded platforms). When current through them is too high, it melts the metal connecting the two blades and the fuse breaks – cutting the power to the circuit in question. The problem is, the fuses must them be replaced. In an automobile this isn’t too problematic as these fuses are cheap but in an embedded system this can mean replacing the whole board. Furthermore, these systems are pessimistic because they can shut down entire networks within a board when only one component is at fault. As such, our problem…

## Slide 7: Approach
Inductor (slows the rise of current)
+
Real-time task (detects shorts by deadline)
=
Software-based real-time short-circuit protection
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: To address this, our approach is to combine an inductor with a real-time task to detect and halt short circuits before they caused damage. An example inductor can be seen on the left (generally coils of copper wire). We’ve taken this approach with the goal of *MAIN IDEA* leveraging physical dynamics to minimize pessimism in real-time systems.

## Slide 8: Contribution Summary
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Notes: Our contributions therefore are a real-time software based short circuit protection method, a relationship between RT util and board space consumed by an inductor (as well as optimization approaches based on this relationship), and finally a simulated and practical evaluation of the proposed methods.

## Slide 9: Outline
Electronics Background
Related Work
System Model
Evaluation and Results
Conclusion
Notes: For the remainder of the presentation, I’ll cover a brief electronics background along with related works in both EE and RT, our proposed system model, evaluation, results, and some concluding notes.

## Slide 10: Electronics Background

## Slide 11: Basic Circuitry
Ohm’s Law:
Background
Short The flow of current through an alternate, unintended path in a circuit with little or no impedance
=
I
R
V
t
I
Notes: As a quick review of basic circuitry, suppose we have a circuit with battery and load, a lightbulb. If we increase the load on the circuit …. Removing the load returns current flow to the nominal current and voltage. Furthermore, we can remove the initial load via a “short”

## Slide 12: Inductors
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Background
Inductor Resists change in current
Schematic Symbol:
Term | Symbol | SI Unit
Inductance | L | Henry (H)
t
I
Notes: Most important chrematistic is its ability to resist changes in current.

## Slide 13: DC-RL Circuits
Direct Current (DC)
+
Resistor-Inductor (RL)
=
DC-RL
Background
Notes: We can transform this example into the model we’ll use later: a DC-RL Circuit

## Slide 14: Detailed Approach
Requires:
  Inductor
  Real-Time Task
Allows:
  Short-circuit protection
  Trading inductance (size) with task utilization
Approach

## Slide 15: Related Work
S. Hain and M. M. Bakran [6] Horiguchi et. al. [9] Wang et. al. [18]
Related Work
Krone et. al. [13]
Detection in Hardware
Inductors
No Inductors
Detection in Software
This Work
?

## Slide 16: System Model

## Slide 17: Inductors: Spatial Parameters
Term | Symbol | SI Unit
Inductance | L | Henry (H)
System Model
Notes: This is a spatial representation of a solenoid-style inductor (solenoid meaning a coil of wire that extends some length l).

## Slide 18: Quick Summary
System Model
In practice, what do short-circuits with an inductor look like?
Notes: As a quick review, we have a DC-RL circuit discussed earlier. It contains an inductor that we can model based on its spatial characteristics. So… what’s…

## Slide 19: Electronics System: Example Short Detection
System Model
DetectionSignal
Circuit Voltage
Voltage
Time
Notes: To answer that, let’s look at an example short detection.

## Slide 20: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.

## Slide 21: Methods of Detection: Maximum I
System Model
Maximum Current
Critical Current
Gap
Notes: Based on the OCM mentioned earlier, we can extract two methods for catching shorts. The most obvious is….

## Slide 22: Methods of Detection: Maximum ∆I
Maximum ∆I L
System Model
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Notes: A less obvious method of detection is using the maximum change in I. Slope of the line is proportional to inductance. Allows for detection long before even the maximum current is reached.

## Slide 23: Quick Summary
System Model
Maximum ∆I L
Maximum Current
Max I Detection
Max ∆I Detection
How much time do we have to catch a short-circuit?

## Slide 24: Methods of Detection: Min. Time to Detection
System Model
Smallest Gap
Maximum ∆I
How do we translate this into a real-time task?
Crit. Current
Max. Current
Notes: To be effective and safe, our system must handle the worst case gracefully. This worst case comes when the smallest gap between maximum and critical currents is crossed using the maximum change in I allowed. To address this, we take the I_crit – I_max and divide by \Delta I giving us the fastest time a short circuit can cause damage and thus the maximum latency allowed for a successful short-detection.

## Slide 25: Real-Time System Model
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Intuition
System Model
Smallest Gap
Max I Detection
Max ∆I Detection
Maximum ∆ I
Notes: We use a sporadic task model in which …
To illustrate the importance of this ½ term we’ll look at an unsuccessful detection schedule…

## Slide 26: Real-Time System Model: Example Failure
don’t divide by 2
System Model
Suppose period = δ = 4
Notes: We miss the short detection because the maximum time between consecutive jobs exceeds the minimum time to detection.

## Slide 27: Real-Time System Model: Example Success
System Model
do divide by 2
Suppose period = = 2
Notes: Dividing by two guarantees detection in time, even if the short occurs instantaneously before the release.

## Slide 28: Real-Time System Model: Utilization
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Earliest Deadline First Utilization Constraint:
Task Utilization:
System Model
Notes: Some quick math gives us our task utilization where our execution time is divided by period.

## Slide 29: Quick Model Summary
System Model
Min. Time to Detection
Maximum ∆I
Crit. Current
Max. Current

## Slide 30: Inductance vs Utilization Relationship
System Model
Short-circuit task utilization may be traded with inductor size and thus board space consumed
Primary Contribution:
Maximum ∆I L
Notes: The primary contribution now comes from combining these previously distinct areas of hardware and scheduling to build a fluid relationship.

## Slide 31: Evaluation and Results

## Slide 32: Experiment Setup
Evaluation
Processor: PIC18F45K20 Speed: 64MHz ADC: 10-bit

## Slide 33: Experimentation: FUL and HSF Shorts
Experiment 1 : Fault Under Load (FUL); Experiment 2 : Hard-Switching Fault (HSF)
Critical current is 150 mA
Evaluation
Notes: Here are the results of our experimentation. Note that the current at the time of detection is well below the allowed limit and our utilization is nearly 10%. No smaller utilization was allowed.

## Slide 34: Experimentation: Scaling
Smaller utilization
=
larger current at time of detection
Smaller inductance
= larger current at time of detection
Evaluation
Notes: Plotting the results of our experiments, we see two correlations are established. Together, these correlations establish that an increase in utilization is complemented with a decrease in inductance and vice versa.

## Slide 35: Short Detection with Varied Period
Evaluation
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: We also demonstrate that short detection can occur with a varied period, especially if the circuit experiences changes in power input it may adjust accordingly thereby sampling only as frequently as necessary based on input. So when no power is running, minimal sampling is needed.

## Slide 36: Conclusion

## Slide 37: Contribution Summary and Future Work
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion

## Slide 38: Previous Publication
Honors Sr. Thesis, Wayne State University, Detroit, USA. May 2016
  Advisor: Prof. Nathan Fisher
23rd IEEE International Conference on Embedded and Real-Time Computing Systems and Applications, Hsinchu, Taiwan. Aug. 2017
  Advisor: Prof. Nathan Fisher
Conclusion

## Slide 39: Thank you!
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion
Questions? aaron.willcock@wayne.edu
Disclaimer: No toasters were harmed during this research.

## Slide 42: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
for all
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.