## Slide 1: Demand Characterization and Codesign of Dynamics-Adaptive Real-Time Systems
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 2: Hard Real-Time Systems
Systems which:
require logically and temporally correct results;
incur catastrophic failure when either logical or temporal errors occur;

## Slide 3: Hard Real-Time Systems: Airbags
Simplified Airbag System
Logical Failure:
  Unnecessarily fire airbag
  Fail to fire during accident
Temporal Failure:
  Fire airbag too late
IMU
Wheel Speed Sensor
ECU
Airbag

## Slide 4: Traditional Real-Time Systems
Workloads Broken into Jobs, Tasks

## Slide 5: Traditional Real-Time Systems
Task Sets have demand characterized

## Slide 6: Problem & Motivation
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Variable nature of task parameters makes demand characterization difficult.
Recent research thrusts in Cyber Physical Systems tightly integrate software and hardware.
In Real-Time Systems, this integration has manifested as tasks with adaptive parameters.

## Slide 7: Approach
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL

## Slide 8: Approach
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL
1. Leverage limitations of physical system dynamics to reduce pessimism and increase efficiency of demand characterization

## Slide 9: Approach
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL
1. Leverage limitations of physical system dynamics to reduce pessimism and increase efficiency of demand characterization
2. Establish bidirectional relationships between system dynamics and schedulability to facilitate codesign.

## Slide 10: Thesis
Incorporating physical dynamics into real-time system analysis can reduce pessimism and increase efficiency of demand characterization and schedulability analysis while enabling the codesign of Real-Time, Cyber-Physical Systems

## Slide 11: Related Works (table/box)
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 12: An Efficient Knapsack-Based Approach for Calculating the Worst-Case Demand of AVR Tasks
Sandeep Kumar Bijinemula*, Aaron Willcock†,
Thidapat Chantem*, Nathan Fisher†
*Department of Electrical and Computer Engineering, Virginia Tech, USA
†Department of Computer Science, Wayne State University, USA
Notes: collaboration

## Slide 13: Holiday Thievery
You have 100 seconds to take anything …for free
What would you take?
Where would you start?
Imagine your favorite store.
Notes: Media Markt. For those who recognize, this is akin to the typical knapsack problem.

## Slide 14: Holiday Thievery
Goal:
Maximize value over 100 seconds
Increase value
Decrease time

## Slide 15: Holiday Thievery Function
Items per Second
Value of Items
Engine Control Module (ECM)
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif

## Slide 16
Holiday Thievery Function
Value of Items
Items per Second
Execution Times of the Modes
Speeds
Engine Control: Adaptive Variable-Rate (AVR) Tasks
Engine Control Module (ECM)
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif
c – execution time
– angular speed
Biondi et al. [ICCPS ‘15]

## Slide 17: Engine Control: Adaptive Variable-Rate (AVR) Tasks
Speeds
Execution Times of the Modes
Higher rate of job release
Less time between job releases
Higher rate of job release
Lower WCET per job
c – execution time
– angular speed
Jobs released at Top Dead Center (TDC)
Jobs due in one revolution (one full rotation)
Biondi et al. [ICCPS ‘15]

## Slide 18: Engine Control: Adaptive Variable-Rate (AVR) Tasks
Speeds
Execution Times of the Modes
Higher rate of job release
More time between job releases
Higher rate of job release
Higher WCET per job
c – execution time
– angular speed
Jobs released at Top Dead Center (TDC)
Jobs due in one revolution (one full rotation)
Biondi et al. [ICCPS ‘15]
But how do we calculate worst-case demand?
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 19: Demand of AVR Tasks
Speeds
Execution Times of the Modes
Calculation of worst-case demand is not straightforward.
Engine Control: Adaptive Variable-Rate (AVR) Tasks
c – execution time
– angular speed
Which point gives the worst-case demand?
Biondi et al. [ICCPS ‘15]
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.
We call the stretches of equal value "modes" or "steps" and the rightmost edge of the "step" a "right boundary".

## Slide 20: Demand of AVR Tasks
Speeds
Execution Times of the Modes
Calculation of worst-case demand is not straightforward.
c – execution time
– angular speed
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 21: Motivation and Problem Statement
Speeds
Execution Times of the Modes
Existing calculations of exact worst-case demand for AVR tasks are compute intensive.
Motivation:
Calculate the exact worst-case demand of an AVR task over a time interval .
Problem Statement:
Demand of AVR Tasks
c – execution time
– angular speed
?
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 22: Approach & Contributions
1. Worst-case AVR task demand ↔ Bounded precedence constraint knapsack problem (BPCKP).
2. Symmetric acceleration + Engine kinematics →
Reduced search space.
3. Results significantly outperform the state-of-the-art in computation time.
↔
→
?
Notes: "We make a simplifying assumption that magnitude of acceleration and deceleration is equal"

## Slide 23: Outline
Approach and Contributions
Background & Related Work
Precedence Constraints & Search Space Reduction
Worst-Case AVR Demand as Knapsack Problem
Evaluation & Results
Conclusion & Future Work

## Slide 24: Background & Related Work

## Slide 25: AVR Tasks – Speed or WCET?
Speeds
Execution Times of the Modes
c – execution time
– angular speed
+ Allows WCET to scale inversely with speed
? How can we calculate worst-case demand?
Right Boundary (RB) RB Speeds ()
Modes / Steps
Biondi et al. [ICCPS ‘15]

## Slide 26: Digraph Real-Time (DRT) Approach
Speeds
Execution Times of the Modes
+ Exact worst-case demand for a select set of speeds
? How can we compute worst-case demand faster?
Mohaqeqi et al. [ECRTS ‘17]
c – execution time
– angular speed
AVR Tasks – Speed or WCET?

## Slide 27: Related Works
Model – Adaptive-Variable Rate / Rhythmic Biondi et al. [ICCPS ‘15], Kim et al. [ICCPS ‘12]
Schedulability Guo and Baruah [ICCPS ‘15]
Exact Worst-case Demand Biondi et al. [ECRTS ‘14]
Exact Worst-case Demand via DRT Mohaqeqi et al. [ECRTS ‘17]
Constant Acceleration between Jobs
Variable Acceleration between Jobs
Exact Worst-case Demand via Knapsack
(This work)

## Slide 28: Related Works
Model – Adaptive-Variable Rate / Rhythmic Biondi et al. [ICCPS ‘15], Kim et al. [ICCPS ‘12]
Schedulability Guo and Baruah [ICCPS ‘15]
Exact Worst-case Demand Biondi et al. [ECRTS ‘14]
Exact Worst-case Demand via DRT Mohaqeqi et al. [ECRTS ‘17]
Constant Acceleration between Jobs
Variable Acceleration between Jobs
Exact Worst-case Demand via Knapsack
(This work)
= maximum deceleration
= maximum acceleration

## Slide 29: Outline
Approach and Contributions
Background & Related Work
Precedence Constraints & Search Space Reduction
Worst-Case AVR Demand as Knapsack Problem
Evaluation & Results
Conclusion & Future Work
Notes: Overview

## Slide 30: Precedence Constraints & Search Space Reduction

## Slide 31: Acceleration Limits (on AVR)
Execution Times of the Modes
c – execution time
– angular speed
Reachable Speeds
Notes: Consider the AVR graph that we are familiar from the previous slides.

## Slide 32: Search Space Reduction: Dominant Sequences
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: To help us reduce the search space, we rely on the concept of “Dominant Sequences”. A dominant sequence is…

## Slide 33: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: To visualize the need for these sequences, suppose we have three separate sequences. Each sequence with slight variations from the others. Some only decrease, some use variable acceleration, and some use only maximum acceleration.​

## Slide 34: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: We prove characteristics of dominant sequences that allow us to compare these sequences...​

## Slide 35: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
We only search for dominant sequences!
Notes: … and establish which sequence maximizes demand over the same timer interval. Because of this, we only search for dominant sequences across the range of available speeds.​

## Slide 36: Properties of a Dominant Sequence
Lemma 1 : Dominant sequences do not contain any decreasing subsequences.
Max. Accel. ()
Max. Decel. ()
Var. Accel.
Speeds
Speeds
Decreasing sequences can be transformed into non-decreasing sequences with equal or greater demand!
Lemma 1: Only non-decreasing sequences allowed.
Notes: Lemma 1 says that

## Slide 37: Properties of a Dominant Sequence
n jobs in the middle of a step
n jobs at the right boundary speed
Same execution time, shorter time
Lemma 2 : The first job of a dominant sequence begins at a right boundary.
Lemma 2: Start at a right boundary speed (RB).
Notes: Lemma 2 says

## Slide 38: Properties of a Dominant Sequence
Use Max. Accel.
Option 2
Single Var. Accel.
When travels past right boundary, variable accel. may be used.
Option 1 Max. Accel.
RBs Multiple and
Max. Accel.
Decision Speed
n
Lemma 3 : Dominant sequences have fixed choices for next speeds.
Lemma 3: Use maximum acceleration. Additionally, at decision speeds, use variable acceleration to reach RB.
Can release multiple jobs at RB.
Notes: Lemma 3 gives us the choice of speeds given the current speed

## Slide 39: Dominant Sequence Visualization
Speeds
Execution Times of the Modes
Notes: To put the lemmas into context, we will now visualize the dominant sequence

## Slide 40: Dominant Sequence Visualization
Lemma 1: Only non-decreasing sequences allowed.
Lemma 2: Start at a right boundary speed (RB).
Lemma 3: Use maximum acceleration. Additionally, at decision speeds, use variable acceleration to reach RB.
Can release multiple jobs at RB.
Max. Accel. ()
Max. Decel. ()
Var. Accel.

## Slide 41: A Visual Comparison
Sequences in previous work
Sequence in our approach
Search space in our approach is significantly reduced.
Notes: To put this in perspective, we compare our approach with the DRT approach

## Slide 42: Worst-Case Demand as Knapsack
Notes: We now transform the problem into…

## Slide 43: Jobs as Items, Time as Knapsack
ID
Profit
Weight
Item #1
$ 2
17 kg
Initial Speed,
Final Speed
WCET
Min. Interarrival (time)
Knapsack = Duration of time
Max 100 kg
Max 100 sec.
43
Notes: In the traditional knapsack problem….

## Slide 44: Transformation Visualization
Speeds
Execution Times of the Modes
t
0
Precedence Constraints should be followed too
t
0
Notes: Let us visualize the transformation…

## Slide 45
(, )
(, )
()
()
()
()
()
()
(, )
BPCKP
Decision Speed
– Execution time
- Job inter-arrival time
Right boundary speed
Middle of a step
Bounded Precedence Constraint Knapsack Problem

## Slide 46
(, )
(, )
()
()
()
()
()
()
(, )
BPCKP
Multiple jobs at RBs –Restricted by the length of the time-interval
Solve the resultant BPCKP with Dynamic Programming
– Execution time
- Job inter-arrival time
Notes: We mention that multiple jobs can be released at the right boundary speeds.

## Slide 47: Time complexity
Number of Unique Items in Knapsack:
Search complexity – Pseudo polynomial
  Same as any bounded precedence constraint knapsack problem
– number of modes
Notes: We share a similar complexity when to calculating the number of unique items in the knapsack with the DRT approach.

## Slide 48: Evaluation and Results
Notes: We now move on to the results section

## Slide 49: AVR Task Set: Table Comparison
Task Set in Previous Work
A More Challenging Task Set
is reachable from in integer rotations
Decreases the number of decision speeds
is not reachable from in integer rotations
mode | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 500 | 1500 | 2500 | 3500 | 4500 | 5500 | 6500
 | 965 | 576 | 424 | 343 | 277 | 246 | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 500 | 1500 | 2500 | 3500 | 4500 | 5500 | 6500
 | 965 | 576 | 424 | 343 | 277 | 246 | 
mode | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 1200 | 2200 | 3200 | 4200 | 5200 | 6200 | 7200
 | 965 | 576 | 424 | 343 | 277 | 246 | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 1200 | 2200 | 3200 | 4200 | 5200 | 6200 | 7200
 | 965 | 576 | 424 | 343 | 277 | 246 | 
Notes: The problem statement of our approach…

## Slide 50: AVR Task Set: Visual Comparison
Previous Work Task Set
Fewer sequences
in the search space
More Challenging Task Set
More sequences in the search space
# Decision Speeds less than # Modes
# Decision Speeds equal to # Modes
Notes: To visualize this

## Slide 51: Algorithm Runtime Comparison
 | Previous Task Set | More Challenging Task Set
DRT Alg. | 3 min. 31 sec. | 17 min. 2 sec.
Our Alg. | 15.63 sec. | 19.24 sec.
Performance Improvement | 13.5 | 53.1
System: Python 3.6.5, 3.4 GHz quad-core processor, 8 GB RAM
Experiment: Calculate worst-case demand for 100 intervals from [0,1s]

## Slide 52: Random Taskset Alg. Runtimes

## Slide 53: Public Artifact
http://bit.ly/ RTSS18KAVR
Recreate paper results
Customize task sets
Graphical comparison
Python w/ Markdown documentation

## Slide 54: Engine Control Future Work
Relax the symmetric acceleration assumptions
~
θ
Additional problem dimensions
AVR tasks with different phases
Approximation algorithms
Notes: For future work, we aim to relax the symmetric acceleration assumptions, increase the number of problem dimensions to include things like temperature and pressure, apply approximation algorithms to the knapsack approach, and handle AVR tasks with different phases.

## Slide 55: Engine Control Conclusion
1. Worst-case AVR task demand ↔ Bounded precedence constraint knapsack problem (BPCKP).
2. Symmetric acceleration + Engine kinematics → Reduced search space.
3. Results significantly outperform the state-of-the-art in computation time.
↔
→
http://bit.ly/RTSS18KAVR
sandeepb@vt.edu
aaron.willcock@wayne.edu
tchantem@vt.edu
fishern@wayne.edu
Questions?
?
Notes: "We make a simplifying assumption that magnitude of acceleration and deceleration is equal"

## Slide 56: Future Work
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 57: Timeline

## Slide 58: Publications
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 59: Concluding Summary
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 60: Appendix

## Slide 61: Random Taskset Alg. Runtimes (Log)

## Slide 62: Rand. Taskset Knapsack Runtimes

## Slide 63: Standalone AVR Function
Speeds
Execution Times of the modes
c – execution time
– angular speed
Biondi et al. [ICCPS ‘15]

## Slide 64: Why assume ?
1. How does the problem change when ?
3. What intuitions can we gather about DRT vs BPCKP?
4. How can we better map the solution space?
2. Are there non-trivial exploits?

## Slide 65: But my [insert rotational source] doesn’t have symmetric acceleration!
Increase magnitude of the lesser to match the larger.
Gives pessimistic worst-case demand for the original, asymmetric system.

## Slide 66: But my [insert rotational source] doesn’t have symmetric acceleration!
Imagine a set of asymmetric systems.
Systems where artificially raise .
Systems where artificially raise .
Gives pessimistic worst-case demand for the original, asymmetric system.

## Slide 67: How does this compare to actual internal combustion engines?
Internal Combustion Engine Fundamentals, 2nd Edition by J.B. Heywood
Most internal combustion engines operating without load fall in the highlighted category.
Typically >>
since friction is the primary cause of

## Slide 68: Trading Utilization for Circuitry: Hardware-Software Co-design for Real-Time Software-Based Short-Circuit Protection
Aaron Willcock
Department of Computer Science, Wayne State University, USA

## Slide 69: Toast, anyone?
?
?
Notes: Have you ever been tempted to toss a toaster into the tub?
Perhaps silverware in a socket is more your style?
You don’t have to admit it here. But if you found yourself considering it, know that there are safety mechanisms to stop the short circuits you’d create making it much less exciting.

## Slide 70: Not Your Fault
Ground Fault Interrupter
Fuse Box
Image Provided by: Dimitry G https://commons.wikimedia.org/wiki/File:Fuse_box_after_finishing.JPG
Goal: Stop short circuits, avoid damage (death) via fixed hardware
Notes: If your house or apartment was constructed more recently, it likely has Ground Fault Interrupters and Fuse Boxes aimed at stopping short circuits before they cause damage. These protection mechanisms, however, is fixed hardware. This is not the Internet of Things nor a SMART home feature.

## Slide 71: Your Home is Not Alone
Home Applications:
  Photovoltaics
Industrial Electronics:
  Devices using Insulated Gate Bipolar Transistors (IGBTs)
In General:
  Power Converters / Inverters (AC → DC, DC → AC)
Notes: But your home is not alone in this short-protection technology. Outside the house, photovoltaic systems require short protection as do industrial electronics like IGBTs. In general, systems that conduct power conversion have some short-circuit hardware in place to prevent damage and death.

## Slide 72: Low Power, High Stakes
Embedded systems need protection
Ex. Samsung Galaxy Note 7
  Batteries caught fire
  Device banned by FAA
  Root cause: short circuits
Image Provided by: Independent.co.uk https://www.independent.co.uk/life-style/gadgets-and-tech/news/samsung-galaxy-note-7-return-refund-exploding-fire-brand-recall-a7361216.html
Notes: Short circuits are not just a problem for houses. Embedded systems need protection as well! As an example, the Samsung galaxy note 7 made headlines when its batteries caught fire or exploded. The device was even banned by the FAA. After internal investigations, Samsung declared short circuits in the battery as the cause. Despite the lower power, short circuits can still cause substantial damage

## Slide 73: Motivation and Problem Statement
Image Provided by: WEETECH Inc.
https://www.weetech-usa.com/applications/ automotive/relay-and-fuse-box/
Short
  Damage
  Time-sensitive
Dedicated circuitry
  Inflexible
  Costly
  Pessimistic
Existing short-circuit protection for embedded systems is fixed, inflexible and does not consider software-based real-time control.
Problem Statement:
Notes: It’s well established that short circuits can cause damage and even death. What’s worse is that hardware-based approaches are inflexible, costly, and pessimistic. Consider automotive fuses for example. These fuses consume a great deal of space in a vehicle (and similarly in embedded platforms). When current through them is too high, it melts the metal connecting the two blades and the fuse breaks – cutting the power to the circuit in question. The problem is, the fuses must them be replaced. In an automobile this isn’t too problematic as these fuses are cheap but in an embedded system this can mean replacing the whole board. Furthermore, these systems are pessimistic because they can shut down entire networks within a board when only one component is at fault. As such, our problem…

## Slide 74: Approach
Inductor (slows the rise of current)
+
Real-time task (detects shorts by deadline)
=
Software-based real-time short-circuit protection
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: To address this, our approach is to combine an inductor with a real-time task to detect and halt short circuits before they caused damage. An example inductor can be seen on the left (generally coils of copper wire). We’ve taken this approach with the goal of *MAIN IDEA* leveraging physical dynamics to minimize pessimism in real-time systems.

## Slide 75: Contribution Summary
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Notes: Our contributions therefore are a real-time software based short circuit protection method, a relationship between RT util and board space consumed by an inductor (as well as optimization approaches based on this relationship), and finally a simulated and practical evaluation of the proposed methods.

## Slide 76: Outline
Electronics Background
Related Work
System Model
Evaluation and Results
Conclusion
Notes: For the remainder of the presentation, I’ll cover a brief electronics background along with related works in both EE and RT, our proposed system model, evaluation, results, and some concluding notes.

## Slide 77: Electronics Background

## Slide 78: Basic Circuitry
Ohm’s Law:
Background
Short The flow of current through an alternate, unintended path in a circuit with little or no impedance
=
I
R
V
t
I
Notes: As a quick review of basic circuitry, suppose we have a circuit with battery and load, a lightbulb. If we increase the load on the circuit …. Removing the load returns current flow to the nominal current and voltage. Furthermore, we can remove the initial load via a “short”

## Slide 79: Inductors
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Background
Inductor Resists change in current
Schematic Symbol:
Term | Symbol | SI Unit
Inductance | L | Henry (H)
t
I
Notes: Most important chrematistic is its ability to resist changes in current.

## Slide 80: DC-RL Circuits
Direct Current (DC)
+
Resistor-Inductor (RL)
=
DC-RL
Background
Notes: We can transform this example into the model we’ll use later: a DC-RL Circuit

## Slide 81: Detailed Approach
Requires:
  Inductor
  Real-Time Task
Allows:
  Short-circuit protection
  Trading inductance (size) with task utilization
Approach

## Slide 82: Related Work
S. Hain and M. M. Bakran [6] Horiguchi et. al. [9] Wang et. al. [18]
Related Work
Krone et. al. [13]
Detection in Hardware
Inductors
No Inductors
Detection in Software
This Work
?

## Slide 83: System Model

## Slide 84: Inductors: Spatial Parameters
Term | Symbol | SI Unit
Inductance | L | Henry (H)
System Model
Notes: This is a spatial representation of a solenoid-style inductor (solenoid meaning a coil of wire that extends some length l).

## Slide 85: Quick Summary
System Model
In practice, what do short-circuits with an inductor look like?
Notes: As a quick review, we have a DC-RL circuit discussed earlier. It contains an inductor that we can model based on its spatial characteristics. So… what’s…

## Slide 86: Electronics System: Example Short Detection
System Model
DetectionSignal
Circuit Voltage
Voltage
Time
Notes: To answer that, let’s look at an example short detection.

## Slide 87: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.

## Slide 88: Methods of Detection: Maximum I
System Model
Maximum Current
Critical Current
Gap
Notes: Based on the OCM mentioned earlier, we can extract two methods for catching shorts. The most obvious is….

## Slide 89: Methods of Detection: Maximum ∆I
Maximum ∆I L
System Model
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Notes: A less obvious method of detection is using the maximum change in I. Slope of the line is proportional to inductance. Allows for detection long before even the maximum current is reached.

## Slide 90: Quick Summary
System Model
Maximum ∆I L
Maximum Current
Max I Detection
Max ∆I Detection
How much time do we have to catch a short-circuit?

## Slide 91: Methods of Detection: Min. Time to Detection
System Model
Smallest Gap
Maximum ∆I
How do we translate this into a real-time task?
Crit. Current
Max. Current
Notes: To be effective and safe, our system must handle the worst case gracefully. This worst case comes when the smallest gap between maximum and critical currents is crossed using the maximum change in I allowed. To address this, we take the I_crit – I_max and divide by \Delta I giving us the fastest time a short circuit can cause damage and thus the maximum latency allowed for a successful short-detection.

## Slide 92: Real-Time System Model
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Intuition
System Model
Smallest Gap
Max I Detection
Max ∆I Detection
Maximum ∆ I
Notes: We use a sporadic task model in which …
To illustrate the importance of this ½ term we’ll look at an unsuccessful detection schedule…

## Slide 93: Real-Time System Model: Example Failure
don’t divide by 2
System Model
Suppose period = δ = 4
Notes: We miss the short detection because the maximum time between consecutive jobs exceeds the minimum time to detection.

## Slide 94: Real-Time System Model: Example Success
System Model
do divide by 2
Suppose period = = 2
Notes: Dividing by two guarantees detection in time, even if the short occurs instantaneously before the release.

## Slide 95: Real-Time System Model: Utilization
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Earliest Deadline First Utilization Constraint:
Task Utilization:
System Model
Notes: Some quick math gives us our task utilization where our execution time is divided by period.

## Slide 96: Quick Model Summary
System Model
Min. Time to Detection
Maximum ∆I
Crit. Current
Max. Current

## Slide 97: Inductance vs Utilization Relationship
System Model
Short-circuit task utilization may be traded with inductor size and thus board space consumed
Primary Contribution:
Maximum ∆I L
Notes: The primary contribution now comes from combining these previously distinct areas of hardware and scheduling to build a fluid relationship.

## Slide 98: Evaluation and Results

## Slide 99: Experiment Setup
Evaluation
Processor: PIC18F45K20 Speed: 64MHz ADC: 10-bit

## Slide 100: Experimentation: FUL and HSF Shorts
Experiment 1 : Fault Under Load (FUL); Experiment 2 : Hard-Switching Fault (HSF)
Critical current is 150 mA
Evaluation
Notes: Here are the results of our experimentation. Note that the current at the time of detection is well below the allowed limit and our utilization is nearly 10%. No smaller utilization was allowed.

## Slide 101: Experimentation: Scaling
Smaller utilization
=
larger current at time of detection
Smaller inductance
= larger current at time of detection
Evaluation
Notes: Plotting the results of our experiments, we see two correlations are established. Together, these correlations establish that an increase in utilization is complemented with a decrease in inductance and vice versa.

## Slide 102: Short Detection with Varied Period
Evaluation
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: We also demonstrate that short detection can occur with a varied period, especially if the circuit experiences changes in power input it may adjust accordingly thereby sampling only as frequently as necessary based on input. So when no power is running, minimal sampling is needed.

## Slide 103: Conclusion

## Slide 104: Contribution Summary and Future Work
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion

## Slide 105: Previous Publication
Honors Sr. Thesis, Wayne State University, Detroit, USA. May 2016
  Advisor: Prof. Nathan Fisher
23rd IEEE International Conference on Embedded and Real-Time Computing Systems and Applications, Hsinchu, Taiwan. Aug. 2017
  Advisor: Prof. Nathan Fisher
Conclusion

## Slide 106: Thank you!
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion
Questions? aaron.willcock@wayne.edu
Disclaimer: No toasters were harmed during this research.

## Slide 109: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
for all
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.