## Slide 1: Demand Characterization and Codesign of Dynamics-Adaptive Real-Time Systems
Prospectus Defense - Aaron Willcock (aaron.willcock@wayne.edu)
Advisor – Professor Nathan Fisher (fishern@wayne.edu)

## Slide 2: Hard Real-Time Systems
Systems which:
require logically and temporally correct results;
incur catastrophic failure when either logical or temporal errors occur;
Image Provided by: National Highwat Traffic Safety Administration.

## Slide 3: Hard Real-Time Systems: Airbags
Simplified Airbag System
Logical Failure:
  Incorrectly fire airbag (when there is no collision)
  Fail to fire during collision
Temporal Failure:
  Fire airbag too early (bag is deflating on impact)
  Fire airbag too late (bag strikes occupant)
IMU
Wheel Speed Sensor
ECU
Airbag
Image Provided by: SparkFun.
Image Provided by: Dorman.
Image Provided by: Pixabay.
Image Provided by: HydraMotorWorks.

## Slide 4: Real-Time Systems: Jobs & Tasks
Tasks Infinite sequence of jobs
Jobs Individual units of computation

## Slide 5: Real-Time Systems: Demand
Demand over time interval is the summed WCET of all jobs with releases and deadlines in the interval .
The Demand Bound Function is the maximum demand generated by task set over any interval of size .

## Slide 6: Problem & Motivation
Demand Char. / Sched. Analysis
Static Tasks
Result
PASS
FAIL
Traditional real-time tasks have static task parameters (ex. )
Simple Test: Is ?

## Slide 7: Problem & Motivation
Dynamics- Adaptive Tasks
Demand Char. / Sched. Analysis
Static Tasks
Result
PASS
FAIL
Recent research thrusts in Cyber Physical Systems tightly integrate software and hardware.
In Real-Time Systems, this integration has manifested as tasks with adaptive parameters.
Physical System
Extracted Dynamics

## Slide 8: Problem & Motivation
Dynamics- Adaptive Tasks
Demand Char. / Sched. Analysis
Result
PASS
FAIL
Tasks with adaptive parameters complicate demand characterization and schedulability analysis by making analysis unintuitive and intractable.
Physical System
Extracted Dynamics

## Slide 9: Problem & Motivation
Tasks with adaptive parameters complicate demand characterization and schedulability analysis by making analysis unintuitive and intractable.
Dynamics- Adaptive Tasks
Demand Char. / Sched. Analysis
Result
PASS
FAIL
Physical System
Extracted Dynamics
Approach

## Slide 10: Approach
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL

## Slide 11: Approach
1. Leverage limitations of physical system dynamics to reduce pessimism and increase efficiency of demand characterization
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL

## Slide 12: Approach
1. Leverage limitations of physical system dynamics to reduce pessimism and increase efficiency of demand characterization
2. Establish bidirectional relationships between system dynamics and schedulability to facilitate codesign.
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL

## Slide 13: Thesis
Incorporating physical dynamics into real-time system analysis can reduce pessimism and increase efficiency of demand characterization and schedulability analysis while enabling the codesign of Real-Time Cyber-Physical Systems
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL

## Slide 14: Related Work: Simple Derivatives
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 15: Related Work: Simple Derivatives
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 16: Related Work: Simple Derivatives
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 17: Related Work: Electromagnetics
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Short Circuit Detection: A Quick Summary
Inductor Model
Mapped to RT Task
Protect Against Short Circuits
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 18: Related Work: Classical Mechanics
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Physical System
Extracted Dynamics
Engine Control Tasks
Engine Control Tasks
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 19: Related Work: What We’ll Cover
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
SCD
covered in MS.
Eng Ctrl.
will be the focus for remainder of presentation.
Notes: Take note of dimensions covered, Derivatives used, Intersection points

## Slide 20: An Efficient Knapsack-Based Approach for Calculating the Worst-Case Demand of AVR Tasks
Sandeep Kumar Bijinemula*, Aaron Willcock†,
Thidapat Chantem*, Nathan Fisher†
*Department of Electrical and Computer Engineering, Virginia Tech, USA
†Department of Computer Science, Wayne State University, USA
Notes: collaboration

## Slide 21: Stealing from Stores
You have 100 seconds to take anything …for free
What would you take?
Where would you start?
Imagine your favorite store.
Notes: Media Markt. For those who recognize, this is akin to the typical knapsack problem.

## Slide 22: Holiday Thievery
Goal:
Maximize value over 100 seconds
Increase value
Decrease time

## Slide 23: Holiday Thievery Function
Items per Second
Value of Items
Engine Control Module (ECM)
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif

## Slide 24
Holiday Thievery Function
Value of Items
Items per Second
Execution Times of the Modes
Speeds
Engine Control: Adaptive Variable-Rate (AVR) Tasks
Engine Control Module (ECM)
Image Provided by: Zephyris.
https://commons.wikimedia.org/wiki/
File:4StrokeEngine_Ortho_3D_Small.gif
c – execution time
– angular speed
Biondi et al. [ICCPS ‘15]

## Slide 25: Engine Control: Adaptive Variable-Rate (AVR) Tasks
Speeds
Execution Times of the Modes
Higher rate of job release
Less time between job releases
Higher rate of job release
Lower WCET per job
c – execution time
– angular speed
Jobs released at Top Dead Center (TDC)
Jobs due in one revolution (one full rotation)
Biondi et al. [ICCPS ‘15]

## Slide 26: Engine Control: Adaptive Variable-Rate (AVR) Tasks
Speeds
Execution Times of the Modes
Higher rate of job release
More time between job releases
Higher rate of job release
Higher WCET per job
26
c – execution time
– angular speed
Jobs released at Top Dead Center (TDC)
Jobs due in one revolution (one full rotation)
Biondi et al. [ICCPS ‘15]
But how do we calculate worst-case demand?
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 27: Demand of AVR Tasks
Speeds
Execution Times of the Modes
Calculation of worst-case demand is not straightforward.
Engine Control: Adaptive Variable-Rate (AVR) Tasks
c – execution time
– angular speed
Which point gives the worst-case demand?
Biondi et al. [ICCPS ‘15]
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.
We call the stretches of equal value "modes" or "steps" and the rightmost edge of the "step" a "right boundary".

## Slide 28: Demand of AVR Tasks
Speeds
Execution Times of the Modes
Calculation of worst-case demand is not straightforward.
c – execution time
– angular speed
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 29: Motivation and Problem Statement
Speeds
Execution Times of the Modes
Existing calculations of exact worst-case demand for AVR tasks are compute intensive.
Motivation:
Calculate the exact worst-case demand of an AVR task over a time interval .
Problem Statement:
Demand of AVR Tasks
c – execution time
– angular speed
?
Reduce algorithm runtime
Notes: These are real-time tasks which model the behavior of engine control tasks.
As engine speed increases, time between jobs decreases and WCET decreases.

## Slide 30: Approach & Contributions
1. Worst-case AVR task demand ↔ Bounded precedence constraint knapsack problem (BPCKP).
2. Symmetric acceleration + Engine kinematics →
Reduced search space.
3. Results significantly outperform the state-of-the-art in computation time.
↔
→
?
Notes: "We make a simplifying assumption that magnitude of acceleration and deceleration is equal"

## Slide 31: Outline
Approach and Contributions
Background & Related Work
Precedence Constraints & Search Space Reduction
Worst-Case AVR Demand as Knapsack Problem
Evaluation & Results
Conclusion & Future Work

## Slide 32: Background & Related Work

## Slide 33: AVR Tasks – Speed or WCET?
Speeds
Execution Times of the Modes
c – execution time
– angular speed
+ Allows WCET to scale inversely with speed
? How can we calculate worst-case demand?
Right Boundary (RB) RB Speeds ()
Modes / Steps
Biondi et al. [ICCPS ‘15]

## Slide 34: Digraph Real-Time (DRT) Approach
Speeds
Execution Times of the Modes
+ Exact worst-case demand for a select set of speeds
? How can we compute worst-case demand faster?
Mohaqeqi et al. [ECRTS ‘17]
c – execution time
– angular speed
AVR Tasks – Speed or WCET?

## Slide 35: Related Works
Model – Adaptive-Variable Rate / Rhythmic Biondi et al. [ICCPS ‘15], Kim et al. [ICCPS ‘12]
Schedulability Guo and Baruah [ICCPS ‘15]
Exact Worst-case Demand Biondi et al. [ECRTS ‘14]
Exact Worst-case Demand via DRT Mohaqeqi et al. [ECRTS ‘17]
Constant Acceleration between Jobs
Variable Acceleration between Jobs
Exact Worst-case Demand via Knapsack
(This work)
Some works focus on constant acceleration
{
We focus on variable acceleration
}

## Slide 36: Related Works
Model – Adaptive-Variable Rate / Rhythmic Biondi et al. [ICCPS ‘15], Kim et al. [ICCPS ‘12]
Schedulability Guo and Baruah [ICCPS ‘15]
Exact Worst-case Demand Biondi et al. [ECRTS ‘14]
Exact Worst-case Demand via DRT Mohaqeqi et al. [ECRTS ‘17]
Constant Acceleration between Jobs
Variable Acceleration between Jobs
Exact Worst-case Demand via Knapsack
(This work)
= maximum deceleration
= maximum acceleration

## Slide 37: Outline
Approach and Contributions
Background & Related Work
Precedence Constraints & Search Space Reduction
Worst-Case AVR Demand as Knapsack Problem
Evaluation & Results
Conclusion & Future Work
Notes: Overview

## Slide 38: Precedence Constraints & Search Space Reduction

## Slide 39: Acceleration Limits (on AVR)
Execution Times of the Modes
c – execution time
– angular speed
Reachable Speeds
Notes: Consider the AVR graph that we are familiar from the previous slides.

## Slide 40: Search Space Reduction: Dominant Sequences
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: To help us reduce the search space, we rely on the concept of “Dominant Sequences”. A dominant sequence is…

## Slide 41: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: To visualize the need for these sequences, suppose we have three separate sequences. Each sequence with slight variations from the others. Some only decrease, some use variable acceleration, and some use only maximum acceleration.​

## Slide 42: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
Notes: We prove characteristics of dominant sequences that allow us to compare these sequences...​

## Slide 43: Dominant Sequence Visualized
Speeds
Execution Times of the Modes
c – execution time
– angular speed
Max. Accel. ()
Max. Decel. ()
Var. Accel.
A dominant sequence is a sequence of job releases which maximizes demand over a time interval .
We only search for dominant sequences!
Notes: … and establish which sequence maximizes demand over the same timer interval. Because of this, we only search for dominant sequences across the range of available speeds.​

## Slide 44: Properties of a Dominant Sequence
Lemma 1 : Dominant sequences do not contain any decreasing subsequences.
Max. Accel. ()
Max. Decel. ()
Var. Accel.
Speeds
Speeds
Decreasing sequences can be transformed into non-decreasing sequences with equal or greater demand!
Lemma 1: Only non-decreasing sequences considered.
Notes: Lemma 1 says that

## Slide 45: Properties of a Dominant Sequence
n jobs in the middle of a step
n jobs at the right boundary speed
Same execution time, shorter time
Lemma 2 : The first job of a dominant sequence begins at a right boundary.
Lemma 2: Start at a right boundary speed (RB).
Notes: Lemma 2 says

## Slide 46: Properties of a Dominant Sequence
Use Max. Accel.
Option 2
Single Var. Accel.
When travels past right boundary, variable accel. may be used.
Option 1 Max. Accel.
RBs Multiple and
Max. Accel.
Decision Speed
n
Lemma 3 : Dominant sequences have fixed choices for next speeds.
Lemma 3: Use maximum acceleration. Additionally, at decision speeds, use variable acceleration to reach RB.
Can release multiple jobs at RB.
Notes: Lemma 3 gives us the choice of speeds given the current speed

## Slide 47: Dominant Sequence Visualization
Speeds
Execution Times of the Modes
Notes: To put the lemmas into context, we will now visualize the dominant sequence

## Slide 48: Dominant Sequence Visualization
Lemma 1: Only non-decreasing sequences considered.
Lemma 2: Start at a right boundary speed (RB).
Lemma 3: Use maximum acceleration. Additionally, at decision speeds, use variable acceleration to reach RB.
Can release multiple jobs at RB.
Max. Accel. ()
Max. Decel. ()
Var. Accel.

## Slide 49: A Visual Comparison
Sequences in previous work
Sequence in our approach
Search space in our approach is significantly reduced.
Notes: To put this in perspective, we compare our approach with the DRT approach

## Slide 50: What’s next?
Lemma 1: Only non-decreasing sequences considered.
Lemma 2: Start at a right boundary speed (RB).
Lemma 3: Use maximum acceleration. Additionally, at decision speeds, use variable acceleration to reach RB.
Can release multiple jobs at RB.
Max. Accel. ()
Max. Decel. ()
Var. Accel.
We now know what a dominant sequence looks like. Now, we need to find dominant sequences.
To find dominant sequences, we look towards the bounded precedence constraint knapsack problem.

## Slide 51: Worst-Case Demand as Knapsack
Notes: We now transform the problem into…

## Slide 52: Jobs as Items, Time as Knapsack
ID
Profit
Weight
Item #1
$ 2
17 kg
Initial Speed,
Final Speed
WCET
Min. Interarrival (time)
Knapsack = Duration of time
Max 100 kg
Max 100 sec.
52
Notes: In the traditional knapsack problem….

## Slide 53: Transformation Visualization
Speeds
Execution Times of the Modes
t
0
Precedence Constraints should be followed too
t
0
Notes: Let us visualize the transformation…

## Slide 54
(, )
(, )
()
()
()
()
()
()
(, )
BPCKP
Decision Speed
– Execution time
- Job inter-arrival time
Right boundary speed
Middle of a step
Bounded Precedence Constraint Knapsack Problem

## Slide 55
(, )
(, )
()
()
()
()
()
()
(, )
BPCKP
Multiple jobs at RBs –Restricted by the length of the time-interval
Solve the resultant BPCKP with Dynamic Programming
– Execution time
- Job inter-arrival time
Notes: We mention that multiple jobs can be released at the right boundary speeds.

## Slide 56: Time complexity
Number of Unique Items in Knapsack:
Search complexity – Pseudo polynomial
  Same as any bounded precedence constraint knapsack problem
– number of modes
Notes: We share a similar complexity when to calculating the number of unique items in the knapsack with the DRT approach.

## Slide 57: Evaluation and Results
Notes: We now move on to the results section

## Slide 58: AVR Task Set: Table Comparison
Task Set in Previous Work
A More Challenging Task Set
is reachable from in integer rotations
Decreases the number of decision speeds
is not reachable from in integer rotations
mode | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 500 | 1500 | 2500 | 3500 | 4500 | 5500 | 6500
 | 965 | 576 | 424 | 343 | 277 | 246 | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 500 | 1500 | 2500 | 3500 | 4500 | 5500 | 6500
 | 965 | 576 | 424 | 343 | 277 | 246 | 
mode | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 1200 | 2200 | 3200 | 4200 | 5200 | 6200 | 7200
 | 965 | 576 | 424 | 343 | 277 | 246 | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 1200 | 2200 | 3200 | 4200 | 5200 | 6200 | 7200
 | 965 | 576 | 424 | 343 | 277 | 246 | 
Notes: The problem statement of our approach…

## Slide 59: AVR Task Set: Visual Comparison
Previous Work Task Set
Fewer sequences
in the search space
More Challenging Task Set
More sequences in the search space
# Decision Speeds less than # Modes
# Decision Speeds equal to # Modes
Notes: To visualize this

## Slide 60: Algorithm Runtime Comparison
 | Previous Task Set | More Challenging Task Set
DRT Alg. | 3 min. 31 sec. | 17 min. 2 sec.
Our Alg. | 15.63 sec. | 19.24 sec.
Performance Improvement | 13.5 | 53.1
System: Python 3.6.5, 3.4 GHz quad-core processor, 8 GB RAM
Experiment: Calculate worst-case demand for 100 intervals from [0,1s]

## Slide 61: Random Taskset Alg. Runtimes

## Slide 62: Public Artifact
http://bit.ly/ RTSS18KAVR
Recreate paper results
Customize task sets
Graphical comparison
Python w/ Markdown documentation

## Slide 63: Engine Control Future Work
Relax the symmetric acceleration assumptions
~
θ
Additional problem dimensions
AVR tasks with different phases
Approximation algorithms
Notes: For future work, we aim to relax the symmetric acceleration assumptions, increase the number of problem dimensions to include things like temperature and pressure, apply approximation algorithms to the knapsack approach, and handle AVR tasks with different phases.

## Slide 64: Engine Control Conclusion
1. Worst-case AVR task demand ↔ Bounded precedence constraint knapsack problem (BPCKP).
2. Symmetric acceleration + Engine kinematics → Reduced search space.
3. Results significantly outperform the state-of-the-art in computation time.
↔
→
http://bit.ly/RTSS18KAVR
?
Notes: "We make a simplifying assumption that magnitude of acceleration and deceleration is equal"

## Slide 65: Engine Control in Perspective
↔
?
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL
→

## Slide 66: Future Work: In Context
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl

## Slide 67: Future Work: DBF of Ascending Execution Sequences
Example Repeated Motion
Example Deburring Robot
Machined Engine Block
Deburring Tool End Effector
Notes: Robots for manufacturing execute repeated operations.

## Slide 68: Future Work: DBF of Ascending Execution Sequences
Example Repeated Motion
Example Deburring Robot
Torque Sensor
Camera
Accelerometer
Gyroscope
Encoder
Not in constant use.
Notes: Robots for manufacturing execute repeated operations.

## Slide 69: Future Work: DBF of Ascending Execution Sequences
Example Repeated Motion
Example Deburring Robot Task Execution
Torque, Encoder Enabled
Camera, Accel, Gyro Enabled
Repeating WCET Sequence
Notes: Robots for manufacturing execute repeated operations.

## Slide 70: Future Work: DBF of Ascending Execution Sequences
Example Repeated Motion
Example Deburring Robot Task Execution
Existing Approaches RWS
Our Preliminary Approach
Generalized Multiframe Model (GMF)
DBF Calc Time:
Right-aligned Windows
DBF Calc Time:
Notes: Robots for manufacturing execute repeated operations.

## Slide 71: Future Work: Short Summary
DBF of Monotonically Ascending Execution Sequences (sample)
  An exploit to accompany the Generalized Multiframe Model
DBF of Short Circuit Protection for Multiple Power Paths
  An extension of our short-circuit work to power distribution panels
MAE
MPP

## Slide 72: Future Work: Short Summary
FPTAS for AVR Task DBF (extension of presented work)
  The approximation algorithm for our AVR work
DBF of AVR Tasks in ICEs with Dynamic-Skip Fire
  DBF for variable displacement approach common in modern ICEs
FPTAS
DSF
~
↔

## Slide 73: Future Work: Short Summary
Online Demand-Based Hybrid Powertrain Configuration
  Scheduling analysis for reconfigurable hybrid and/or electric powertrains
RHP
Complications
Mixed Chemistry
Multiple Power Packs
Example Reconfiguration
When to use which? Which to charge (or fill) first? Who charges who?

## Slide 74: Future Work: In Context
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
DSF/ FPTAS
MAE
RHP
MPP
~

## Slide 75: Timeline & Conferences
Target Date | Publication Type | Project | Target Value
2021-03-03 | Conference | WCD of Monotonically Ascending Execution Sequences (MAE) | ECRTS
2021-04-01 | Journal | DBF of Short Circuit Protection for Multiple Power Paths (MPP) | IEEE ToC
2021-05-01 | Journal | FPTAS for AVR Task DBF (FPTAS) | IEEE ToC
2021-05-25 | Conference | DBF of AVR Tasks in ICEs with Dynamic-Skip Fire (DSF) | RTSS
2021-10-26 | Conference | Online Demand-Based Hybrid Powertrain Configuration (RHP) | RTAS
Abbreviation | Type | Full Name
ECRTS | Conference | Euromicro Conference on Real-Time Systems
RTSS | Conference | Real-Time Systems Symposium
RTAS | Conference | Real-Time and Embedded Technology and Applications Symposium
IEEE ToC | Journal | IEEE Transactions on Computers

## Slide 76: Publications
Conference:
Trading Utilization for Circuitry – RTCSA 2017, Conference
An Efficient Knapsack-Based Approach for Calculating the Worst-Case Demand of AVR Tasks – RTSS 2018, Conference
In Progress:
Worst Case Demand of Monotonically Ascending Execution Sequences – Conference
FPTAS for AVR Task DBF - Journal
↔
~

## Slide 77: Conclusion
Demand Char. / Sched. Analysis
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Result
PASS
FAIL
Incorporating physical dynamics into real-time system analysis can reduce pessimism and increase efficiency of demand characterization and schedulability analysis while enabling the codesign of Real-Time Cyber-Physical Systems
Trading Util. for Circuitry – RTCSA’17
↔
Knapsack AVR - RTSS’18
Completed Work
Future Work
Main Contributions Thus Far
Thesis
Real-time software-based short circuit protection method
Real-time short circuit protection task utilization ↔ Board space consumed.
Simulated and practical evaluation of detection method
Worst-case AVR task demand ↔ Bounded precedence constraint knapsack problem (BPCKP).
Search space reduction for DBF of AVR tasks.

## Slide 78: Appendix

## Slide 79: Future Work: In Context
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
Example System Parameters |  |  | Real-Time Task Parameters |  |  |  |  |  | 
Classical Mechanics | Electro- magnetics | General |  |  |  |  |  |  | 
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
 |  |  |  |  |  | Eng. Ctrl |  | SCD | Eng. Ctrl
DSF/ FPTAS
MAE
RHP
MPP
~

## Slide 80: Random Taskset Alg. Runtimes (Log)

## Slide 81: Rand. Taskset Knapsack Runtimes

## Slide 82: Standalone AVR Function
Speeds
Execution Times of the modes
c – execution time
– angular speed
Biondi et al. [ICCPS ‘15]

## Slide 83: Why assume ?
1. How does the problem change when ?
3. What intuitions can we gather about DRT vs BPCKP?
4. How can we better map the solution space?
2. Are there non-trivial exploits?

## Slide 84: But my [insert rotational source] doesn’t have symmetric acceleration!
Increase magnitude of the lesser to match the larger.
Gives pessimistic worst-case demand for the original, asymmetric system.

## Slide 85: But my [insert rotational source] doesn’t have symmetric acceleration!
Imagine a set of asymmetric systems.
Systems where artificially raise .
Systems where artificially raise .
Gives pessimistic worst-case demand for the original, asymmetric system.

## Slide 86: How does this compare to actual internal combustion engines?
Internal Combustion Engine Fundamentals, 2nd Edition by J.B. Heywood
Most internal combustion engines operating without load fall in the highlighted category.
Typically >>
since friction is the primary cause of

## Slide 87: Trading Utilization for Circuitry: Hardware-Software Co-design for Real-Time Software-Based Short-Circuit Protection
Aaron Willcock
Department of Computer Science, Wayne State University, USA

## Slide 88: Toast, anyone?
?
?
Notes: Have you ever been tempted to toss a toaster into the tub?
Perhaps silverware in a socket is more your style?
You don’t have to admit it here. But if you found yourself considering it, know that there are safety mechanisms to stop the short circuits you’d create making it much less exciting.

## Slide 89: Not Your Fault
Ground Fault Interrupter
Fuse Box
Image Provided by: Dimitry G https://commons.wikimedia.org/wiki/File:Fuse_box_after_finishing.JPG
Goal: Stop short circuits, avoid damage (death) via fixed hardware
Notes: If your house or apartment was constructed more recently, it likely has Ground Fault Interrupters and Fuse Boxes aimed at stopping short circuits before they cause damage. These protection mechanisms, however, is fixed hardware. This is not the Internet of Things nor a SMART home feature.

## Slide 90: Your Home is Not Alone
Home Applications:
  Photovoltaics
Industrial Electronics:
  Devices using Insulated Gate Bipolar Transistors (IGBTs)
In General:
  Power Converters / Inverters (AC → DC, DC → AC)
Notes: But your home is not alone in this short-protection technology. Outside the house, photovoltaic systems require short protection as do industrial electronics like IGBTs. In general, systems that conduct power conversion have some short-circuit hardware in place to prevent damage and death.

## Slide 91: Low Power, High Stakes
Embedded systems need protection
Ex. Samsung Galaxy Note 7
  Batteries caught fire
  Device banned by FAA
  Root cause: short circuits
Image Provided by: Independent.co.uk https://www.independent.co.uk/life-style/gadgets-and-tech/news/samsung-galaxy-note-7-return-refund-exploding-fire-brand-recall-a7361216.html
Notes: Short circuits are not just a problem for houses. Embedded systems need protection as well! As an example, the Samsung galaxy note 7 made headlines when its batteries caught fire or exploded. The device was even banned by the FAA. After internal investigations, Samsung declared short circuits in the battery as the cause. Despite the lower power, short circuits can still cause substantial damage

## Slide 92: Motivation and Problem Statement
Image Provided by: WEETECH Inc.
https://www.weetech-usa.com/applications/ automotive/relay-and-fuse-box/
Short
  Damage
  Time-sensitive
Dedicated circuitry
  Inflexible
  Costly
  Pessimistic
Existing short-circuit protection for embedded systems is fixed, inflexible and does not consider software-based real-time control.
Problem Statement:
Notes: It’s well established that short circuits can cause damage and even death. What’s worse is that hardware-based approaches are inflexible, costly, and pessimistic. Consider automotive fuses for example. These fuses consume a great deal of space in a vehicle (and similarly in embedded platforms). When current through them is too high, it melts the metal connecting the two blades and the fuse breaks – cutting the power to the circuit in question. The problem is, the fuses must them be replaced. In an automobile this isn’t too problematic as these fuses are cheap but in an embedded system this can mean replacing the whole board. Furthermore, these systems are pessimistic because they can shut down entire networks within a board when only one component is at fault. As such, our problem…

## Slide 93: Approach
Inductor (slows the rise of current)
+
Real-time task (detects shorts by deadline)
=
Software-based real-time short-circuit protection
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: To address this, our approach is to combine an inductor with a real-time task to detect and halt short circuits before they caused damage. An example inductor can be seen on the left (generally coils of copper wire). We’ve taken this approach with the goal of *MAIN IDEA* leveraging physical dynamics to minimize pessimism in real-time systems.

## Slide 94: Contribution Summary
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Notes: Our contributions therefore are a real-time software based short circuit protection method, a relationship between RT util and board space consumed by an inductor (as well as optimization approaches based on this relationship), and finally a simulated and practical evaluation of the proposed methods.

## Slide 95: Outline
Electronics Background
Related Work
System Model
Evaluation and Results
Conclusion
Notes: For the remainder of the presentation, I’ll cover a brief electronics background along with related works in both EE and RT, our proposed system model, evaluation, results, and some concluding notes.

## Slide 96: Electronics Background

## Slide 97: Basic Circuitry
Ohm’s Law:
Background
Short The flow of current through an alternate, unintended path in a circuit with little or no impedance
=
I
R
V
t
I
Notes: As a quick review of basic circuitry, suppose we have a circuit with battery and load, a lightbulb. If we increase the load on the circuit …. Removing the load returns current flow to the nominal current and voltage. Furthermore, we can remove the initial load via a “short”

## Slide 98: Inductors
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Background
Inductor Resists change in current
Schematic Symbol:
Term | Symbol | SI Unit
Inductance | L | Henry (H)
t
I
Notes: Most important chrematistic is its ability to resist changes in current.

## Slide 99: DC-RL Circuits
Direct Current (DC)
+
Resistor-Inductor (RL)
=
DC-RL
Background
Notes: We can transform this example into the model we’ll use later: a DC-RL Circuit

## Slide 100: Detailed Approach
Requires:
  Inductor
  Real-Time Task
Allows:
  Short-circuit protection
  Trading inductance (size) with task utilization
Approach

## Slide 101: Related Work
S. Hain and M. M. Bakran [6] Horiguchi et. al. [9] Wang et. al. [18]
Related Work
Krone et. al. [13]
Detection in Hardware
Inductors
No Inductors
Detection in Software
This Work
?

## Slide 102: System Model

## Slide 103: Inductors: Spatial Parameters
Term | Symbol | SI Unit
Inductance | L | Henry (H)
System Model
Notes: This is a spatial representation of a solenoid-style inductor (solenoid meaning a coil of wire that extends some length l).

## Slide 104: Quick Summary
System Model
In practice, what do short-circuits with an inductor look like?
Notes: As a quick review, we have a DC-RL circuit discussed earlier. It contains an inductor that we can model based on its spatial characteristics. So… what’s…

## Slide 105: Electronics System: Example Short Detection
System Model
DetectionSignal
Circuit Voltage
Voltage
Time
Notes: To answer that, let’s look at an example short detection.

## Slide 106: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.

## Slide 107: Methods of Detection: Maximum I
System Model
Maximum Current
Critical Current
Gap
Notes: Based on the OCM mentioned earlier, we can extract two methods for catching shorts. The most obvious is….

## Slide 108: Methods of Detection: Maximum ∆I
Maximum ∆I L
System Model
Image Provided by: me - Photograph, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=1534586
Notes: A less obvious method of detection is using the maximum change in I. Slope of the line is proportional to inductance. Allows for detection long before even the maximum current is reached.

## Slide 109: Quick Summary
System Model
Maximum ∆I L
Maximum Current
Max I Detection
Max ∆I Detection
How much time do we have to catch a short-circuit?

## Slide 110: Methods of Detection: Min. Time to Detection
System Model
Smallest Gap
Maximum ∆I
How do we translate this into a real-time task?
Crit. Current
Max. Current
Notes: To be effective and safe, our system must handle the worst case gracefully. This worst case comes when the smallest gap between maximum and critical currents is crossed using the maximum change in I allowed. To address this, we take the I_crit – I_max and divide by \Delta I giving us the fastest time a short circuit can cause damage and thus the maximum latency allowed for a successful short-detection.

## Slide 111: Real-Time System Model
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Intuition
System Model
Smallest Gap
Max I Detection
Max ∆I Detection
Maximum ∆ I
Notes: We use a sporadic task model in which …
To illustrate the importance of this ½ term we’ll look at an unsuccessful detection schedule…

## Slide 112: Real-Time System Model: Example Failure
don’t divide by 2
System Model
Suppose period = δ = 4
Notes: We miss the short detection because the maximum time between consecutive jobs exceeds the minimum time to detection.

## Slide 113: Real-Time System Model: Example Success
System Model
do divide by 2
Suppose period = = 2
Notes: Dividing by two guarantees detection in time, even if the short occurs instantaneously before the release.

## Slide 114: Real-Time System Model: Utilization
Sporadic Task Model:
WCET for short-circuit algorithm
Implicit deadline:
Earliest Deadline First Utilization Constraint:
Task Utilization:
System Model
Notes: Some quick math gives us our task utilization where our execution time is divided by period.

## Slide 115: Quick Model Summary
System Model
Min. Time to Detection
Maximum ∆I
Crit. Current
Max. Current

## Slide 116: Inductance vs Utilization Relationship
System Model
Short-circuit task utilization may be traded with inductor size and thus board space consumed
Primary Contribution:
Maximum ∆I L
Notes: The primary contribution now comes from combining these previously distinct areas of hardware and scheduling to build a fluid relationship.

## Slide 117: Evaluation and Results

## Slide 118: Experiment Setup
Evaluation
Processor: PIC18F45K20 Speed: 64MHz ADC: 10-bit

## Slide 119: Experimentation: FUL and HSF Shorts
Experiment 1 : Fault Under Load (FUL); Experiment 2 : Hard-Switching Fault (HSF)
Critical current is 150 mA
Evaluation
Notes: Here are the results of our experimentation. Note that the current at the time of detection is well below the allowed limit and our utilization is nearly 10%. No smaller utilization was allowed.

## Slide 120: Experimentation: Scaling
Smaller utilization
=
larger current at time of detection
Smaller inductance
= larger current at time of detection
Evaluation
Notes: Plotting the results of our experiments, we see two correlations are established. Together, these correlations establish that an increase in utilization is complemented with a decrease in inductance and vice versa.

## Slide 121: Short Detection with Varied Period
Evaluation
Leveraging physical dynamics can minimize pessimism in real-time systems
Main Idea
Notes: We also demonstrate that short detection can occur with a varied period, especially if the circuit experiences changes in power input it may adjust accordingly thereby sampling only as frequently as necessary based on input. So when no power is running, minimal sampling is needed.

## Slide 122: Conclusion

## Slide 123: Contribution Summary and Future Work
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion

## Slide 124: Previous Publication
Honors Sr. Thesis, Wayne State University, Detroit, USA. May 2016
  Advisor: Prof. Nathan Fisher
23rd IEEE International Conference on Embedded and Real-Time Computing Systems and Applications, Hsinchu, Taiwan. Aug. 2017
  Advisor: Prof. Nathan Fisher
Conclusion

## Slide 125: Thank you!
Contributions:
Real-time software-based short circuit protection method
Real-time utilization ↔ Board space consumed
Simulated and practical evaluation
Future Work:
Battery management
DC-RLC circuits (Resistor, Inductor, Capacitor)
Power consumption comparison
Conclusion
Questions? aaron.willcock@wayne.edu
Disclaimer: No toasters were harmed during this research.

## Slide 128: Electronics System: Operating Current Model
Operating Currents
Maximum Current
System Model
Critical Current
for all
Notes: Some less obvious characteristics of this graph are the different modes the circuit can operate in. In our homes we use different loads at different times, but it’s important that your house be able to handle even the worst loads to be safe. We model our embedded system similarly.

## Slide 129: Problem & Motivation
Physical System
Extracted Dynamics
Dynamics- Adaptive Tasks
Variable nature of task parameters makes demand characterization difficult.
Recent research thrusts in Cyber Physical Systems tightly integrate software and hardware.
In Real-Time Systems, this integration has manifested as tasks with adaptive parameters.